## Slide 1: Backward Compatible New Options
- ROLL Interim (25th May 2020)

## Slide 2: What is the problem currently?
(Almost every) New RPL extension requires sending new RPL Control Option
Node which does not understand this new option may strip it off
  Node may or may not strip, RFC 6550 does not explicitly state the handling
Example
  Enrollment Priority
    Min priority field needs to be copied downstream even if not understood by node
  Eliding-RPL-Info, AOO Option
    Does not depend on copying the option downstream
    However needs to explicitly strip off the option if not understood

## Slide 3: Expectation
There should be a way for the node to
  Copy the option forward even though it doesn’t understand
  Or Explicitly Drop the option (not message) if it doesn’t understand
    This is what “may” happen currently
There are more possibilities (just like cap flags)
  Drop/Discard the message if option not understood
  Join as 6LN if option not understood:w

## Slide 4: Proposition-1
Use second higher order bit of Option Type to indicate ‘C’ copy-if-not-understood flag
  First high order bit is already used as ‘Secure’ flag
Easy to handle, no change in control overhead
  However cannot handle anymore flags (such as Join/Discard)
0 1 2
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+- - - - - - - -
|S|C| Option Type | Option Length | Option Data
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+- - - - - - - -

## Slide 5: Proposition-2
Use second higher order bit of Option Type to indicate ‘X’ extended Option flag
  Option data starts after flags
Allows to have more flags
  Can satisfy requirements for other flags (Join and Discard flag)
Option Length includes Option Flags and above
  Thus making it backward compatible such that Option can be skipped while traversing
0 1 2
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+- - - - - - -
|S|X| Option Type | Option Length |Option Flags | Option Data
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+- - - - - - -

## Slide 6: Next Step
WG to decide
Add this to mopex draft (not cap draft)
  Make the unknown-option-handling explicit
  Make it mandatory for RPLv2 nodes to understand the new flag(s)